## Slide 1: Volcano Observatory Questionnaire
Sent to 25 Volcano Observatories (15 countries); 16 responded: Australia, France, Greece, Iceland, Indonesia, Italy, Japan, Netherlands, New Zealand, Papua New Guinea, Solomon Islands, Spain, USA (Alaska Volcano Obs), Vanuatu, Trinidad & Tobago. DNR: Ecuador, Nicaragua, Philippines, Portugal, Russia, Tonga, USA (Hawaiian Volcano Obs)
Asked 14 questions and reference papers:
  Volcano: how many, name, tsunami possible?, discussed and addr volcano tsunami hazard?
  Monitoring: networks, best way to monitor for early tsunami detection?, tsunami-specific monitoring instr?, implement TGV warning system?, any data shared with TWC / TSP, FDSN/IRIS DMC, any historical TGV?
  Warning: TGV SOPs?, Any contact with a TWC? Procedures with VAAC?, Submarine Volcano monitoring and alerts?

## Slide 2: VOQ Summary
TGV tsunami warnings currently follow a ‘Detect, then Warn’ procedure only. Requires detection and confirmation ofwave, and may be too late to be useful unless there are many sensors between the volcano and coastal communities.
For significant tsunami, eruption or flank collapse needs be ‘massive,’ but not yet been quantitatively defined.
Hazard Assessment (eruption history, numerical modelling of historical events or worst- case scenarios) - not been conducted for all potential volcanoes.

## Slide 3: VOQ Summary – Monitoring
Volcano Observatories (VO) monitor seismicity, surface deformation (tilt, movement), and geochemistry as eruption indicators.
Two types of triggers for tsunami:
  VAAC notice of activity. VO-VAAC information exchange. Does not include tsunami hazard potential, nor confirm tsunami wave generated. Therefore,it is a pre-alert – tsunami watch .
  Wave detection at coastal or in-water sensors. Confirms wave was generated, and if large enough results in Tsunami Warning. Instruments: coastal sea level gauges and in-water pressure sensors (Elastic beacon, DART or DART-like)
Most VO do not host sea level stations, and thus are not monitoring sea level for tsunamis.

## Slide 4: VOQ Summary – TGV Procedures - IOC
PTWS HTHH Interim (March 2022). PTWC messages triggered by near-by gauge (Nuku’alofa, DART). Forecast scaled by 15 Jan 2022 observations.
CARIBE-EWS testing Volcano Observatory Notice for Tsunami Threat (VONUT) in CARIBEWAVE 2023 (scenario Mt Pelée). Messages by countries and PTWC. Contain Volcanic Activity Summary and closest sea level gauge locations

## Slide 5: VOQ Summary – TGV Procedures - National
Stromboli (2018) – VO Elastic Beacons in ocean, trigger alerts Civil Protection and sounds sirens
Anak Krakatau (2019) – Indonesia BMKG (NTWC) coastal sea level gauges
Australia – BOM SOPs use VAAC notifications
US, Hawaii Island – PTWC uses TIDS deployed on land. ‘Wet sensor’ detects tsunami inundation (from any source)
Japan - SOPs developed case-by-case basis

## Slide 6: VOQ Summary – Warning Arrangements
Tsunami Warnings usually issued by Tsunami Warning Centres (TWC), which receive real-time sea level data for tsunami monitoring. Since most Volcano Observatories (VO) do not have 24x7 operations, they cannot be TWCs.
To date, VO mostly have not worked closely with TWCs. When earthquake, tsunami, volcano monitoring are part of same agency (e.g. New Zealand), TGV SOPs can be coordinated (seamless) to enable efficient warnings. If not, then harder.
Situation similar for science agencies and universities, who may not be aware of tsunami early warning process and SOPs.
Only recently, Stromboli VO been working with Italian NTWC (INGV) for TGV monitoring and warning

## Slide 7: Recommendations and Gaps (1)
All volcanoes mentioned in the questionnaire should be monitored and have processes in place to warn for tsunamis. Should other, potentially tsunamigenic volcanoes become erupting, these should also be monitored and included within the tsunami warning process.
For these TGV, multi-stakeholder meetings should be convened that included science agencies, and volcano and tsunami warning operations centres. For each identified potential source, Worst-case and credible scenario planning discussions should start as soon as possible.
Detect/warn data streams need to be available to designated tsunami monitoring/warning agency (and possibly also to volcano monitoring agency)

## Slide 8: Recommendations and Gaps (2)
Sea level gauges network with real-time continuous data transmission should be deployed close to each identified volcano. One second sampling is recommended for record and automatic detection. Current satellite data transmission intervals of few minutes to 15 minutes used by the global tsunami warning system are inadequate for TGV warnings. Local transmission through radio link, fiber optic, or telephone lines, or other modes should be implemented.
As a first step, the national organization for TGV should be designated for monitoring and warning. The second and third steps are to install monitoring instrumentation and develop SOPs to handle volcanic tsunamis.

## Slide 9: Recommendations and Gaps (3)
TGV warning notification systems should be considered, and when possible, be part of a multi-hazard alert system. Methods to alert persons in remote areas should be considered (such as scientific teams in the field, or recreational hikers)
During period of heightened TGV hazard, consider closing access to vulnerable areas, and when the eruption is imminent and then tsunami hazard high, evacuating populations from specific locations.
Specific TGV signage and evacuation routes should be implemented in all areas that may be impacted by tsunamis generated by volcanoes.

## Slide 10: Recommendations and Gaps (4)
TGV public awareness campaigns should be conducted regularly – the type of awareness activity or pamphlet/flyer and frequency of the activities may be different for the local population compared to transient populations such as tourists.
TGV monitoring and warning system should be implemented in relationship with the NTWC, where such exist.
TGV SOPs for tsunami warning should be linked with the existing Volcano Alert Activity scales.
Recommendation to IOC
IOC should publish the report in an IOC publication in 2023.
Recommendation by TOWS
Ad hoc TGV team should finalize the report mid 2023